## Slide 1
MALL PARKING FLOW
A Discrete-Event Simulation of Entry, Parking & Exit Congestion
CSE 10/L – Modeling and Simulation
Group Members:
Instructor:
Section:
Date:
Department of Arts and Sciences Education · Computer Science Program · UM Visayan Campus, Tagum City

## Slide 2
ITEM 1
Introduction
A parking lot is a queuing system
Vehicles arrive → wait at entry gate → search & park → shop → queue at exit gate → leave.
Each gate lane serves one vehicle at a time; the lot has finite slots.
Congestion (queues) forms whenever demand outpaces service.
Built with Python + SimPy
Discrete-event simulation (DES) models the lot event by event.
Top-down browser dashboard visualizes queues, gates, and slots live.
Two independent axes: Scenario (demand) × Map (gate layout).
Vehicle Journey
Arrive
Entry Queue
Entry Gate
Search & Park
Dwell (shop)
Exit Queue
Exit Gate
Done

## Slide 3
ITEM 2
Problem Definition
Entry Gate Bottleneck
A queue builds when arrivals cluster or the gate is slow. Vehicles wait before they can even enter the lot.
Exit Gate Bottleneck
A queue builds when many vehicles leave at once or exit processing is slow. Can trap parked cars for long periods.
Denials (Lot Full)
When the lot is full, vehicles are denied entry entirely — lost visits for the mall.
Why it matters:
Long waits hurt customer experience and can spill onto public roads. Denials = lost visits. Management needs to know which bottleneck dominates — and whether a second gate lane is worth it.

## Slide 4
ITEM 3
Objectives
1
Analyze queue performance at the entry and exit gates (waiting time and queue length).
2
Measure resource utilization of the entry gate(s), exit gate(s), and parking capacity.
3
Quantify throughput (vehicles completed per hour) and total time-in-system.
4
Compare operational scenarios — different arrival patterns, reduced capacity, slow entry, slow exit — to identify the dominant bottleneck.
5
Compare gate configurations — same demand on 1-gate vs. 2-gate maps ("one cashier vs. two cashiers").

## Slide 5
ITEM 4A
System Model & Design — DES Elements
Entities
Vehicles (cars & motorcycles) — each with arrival time, type, and assigned lane.
Events
Arrival · gate service start/end · gate crossing · search/park · exit request · departure.
Resources
Entry gate(s) and exit gate(s) (SimPy Resource, capacity 1 per lane) + typed parking slot pools.
Queues
Entry queue(s) and exit queue(s), FIFO. Each gate lane has its own queue.
State variables
Per-vehicle state ×11 · queue lengths · slots free/occupied · denied/completed count · sim clock.
Simulation type: discrete-event · single replication per (scenario × map) · deterministic seeded RNG

## Slide 6
ITEM 4A
Two Independent Configuration Axes
SCENARIO (Demand Profile)
How busy the lot is + how fast gates serve.
Sets: # vehicles, arrival pattern, usable slots, entry/exit service times.
5 profiles: baseline, rush_hour, limited_slots, slow_entry, exit_congestion
baseline
rush_hour
limited_slots
slow_entry
exit_congestion
MAP (Gate Layout)
How many entry / exit gate lanes exist (1 or 2 each).
Sets SimPy resource capacity; 2-gate map = 2 parallel single-server lanes.
one_entrance_one_exit
1 entry · 1 exit
two_entrance_one_exit
2 entry · 1 exit
one_entrance_two_exit
1 entry · 2 exit
two_entrance_two_exit
2 entry · 2 exit
×
any
combination

## Slide 7
ITEM 4B
Vehicle Lifecycle — Process Flow
scheduled
entry_queue
approaching
gate
gate_wait
gate_crossing
searching
parked
exit_queue
exiting
done
DENIED
(no compatible slot)
Resources held:
Entry gate: approach → cross. Exit gate: exit service → merge. Parking slot: reserved at gate → released on exit request.
Queue
Gate service
Terminal
Denied branch
State mapping:
scheduled (A) → entry_queue (B) → approaching_gate (D) → gate_wait (E) → gate_crossing (H) → searching (I) → parked (J) → exit_queue (L) → exiting (N/O) → done (P) + denied branch from G

## Slide 8
ITEM 5
Assumptions & Input Data
Deterministic seeded RNG → repeatable results (seed 101–505).
Each gate lane = single server, FIFO; 2-gate map = two parallel lanes.
Cars → car slots; motorcycles → moto slots; denied if no compatible slot.
Search time grows with lot occupancy.
No field data — ranges chosen for realistic observable behavior.
Scenario
Vehs
Slots
Arrival
Entry svc
Exit svc
baseline
44
72
spread
0.7
0.8
rush_hour
60
72
clustered
1.0
0.95
limited_slots
60
16
spread/long
0.75
0.85
slow_entry
50
72
spread
3.2 ★
0.8
exit_congestion
52
72
spread
0.7
4.0 ★
★ = stressed parameter. Map axis is orthogonal — any scenario runs on any of the 4 gate layouts.

## Slide 9
ITEM 6
Live Demonstration
1
Start baseline / one_entrance_one_exit
Point out: entry queue → gate → search → park → dwell → exit queue → exit.
2
Switch to rush_hour
Watch the entry queue spike to 55. Same capacity, clustering is the stressor.
3
Switch to limited_slots
Show DENIED vehicles and the denied counter. 13 denials, 100% occupancy.
4
Switch maps (e.g. two_entrance_one_exit on slow_entry)
Change only the map — entry wait drops 127 → 52 min. Same demand, more capacity.
5
Custom Inputs panel
Adjust vehicle count, slots, service times, gate count live → Apply & Run.
⚠ Be ready to change scenario, map, or custom inputs on request — that covers 'modify inputs during questioning.'

## Slide 10
ITEM 7A
Results — Five Scenarios (one_entrance_one_exit map)
Metric
baseline
rush_hour
limited_slots
slow_entry
exit_congestion
Avg entry wait (min)
49.5
108.7
69.0
127.0
57.2
Avg exit wait (min)
33.7
37.6
45.0
5.5
119.0
Time in system (min)
131.5
195.4
182.8
183.5
228.8
Throughput (veh/hr)
9.7
10.0
7.5
8.4
6.5
Entry gate util %
58
66
58
86
39
Exit gate util %
80
85
80
69
89
Max exit queue
13
15
18
4
29
Denied vehicles
0
0
13
0
0
Highlighted cells = highest / worst value per metric. Gate utilization identifies the bottleneck: ~86–89% = the limiter.

## Slide 11
ITEM 7B — COMPARISON 1
Scenario Comparison
Chart: 
| baseline | rush_hour | limited_slots | slow_entry | exit_congestion
Avg entry wait (min) | 49.5 | 108.7 | 69 | 127 | 57.2
Avg Entry Wait (min)
Chart: 
| baseline | rush_hour | limited_slots | slow_entry | exit_congestion
Avg exit wait (min) | 33.7 | 37.6 | 45 | 5.5 | 119
Avg Exit Wait (min)
slow_entry vs exit_congestion
Same arrival load — opposite bottleneck. Entry util 86% vs Exit util 89%. Each slow gate becomes the high-util / high-wait resource while the other idles.
baseline vs rush_hour
Same total capacity, same gate speed. Clustered arrivals push entry wait from 49→109 min and peak entry queue from 25→55. Pattern, not capacity, is the stressor.

## Slide 12
ITEM 7B — COMPARISON 2
Gate Configuration — "One Cashier vs. Two Cashiers"
−59%
slow_entry: +1 entry gate
127→52
entry wait: 127 → 52 min
−85%
exit_congestion: +1 exit gate
119→18
exit wait: 119 → 18 min
Chart: 
| 1 entrance 1 exit | 2 entrance 1 exit | 1 entrance 2 exit | 2 entrance 2 exit
slow_entry: entry wait across maps | 127 | 52.1 | 127.2 | 52
slow_entry — Avg Entry Wait (min) by map
Chart: 
| 1 entrance 1 exit | 2 entrance 1 exit | 1 entrance 2 exit | 2 entrance 2 exit
exit_congestion: exit wait across maps | 119 | 154.3 | 18.2 | 54
exit_congestion — Avg Exit Wait (min) by map
⚠ Adding a gate only helps at the bottleneck. For exit_congestion, a second entry gate made exit wait WORSE (119→154 min) — it fed the jammed exit faster.

## Slide 13
ITEM 8
Conclusion & Recommendations
Key Findings
Gate utilization identifies the bottleneck (~86–89% = the limiter).
Arrival clustering inflates waits even with adequate capacity.
Parking capacity is a separate constraint — causes denials regardless of gate speed.
Adding a gate lane only helps at the bottleneck; adding it elsewhere can make things worse.
Recommendations
Add a second lane at the bottleneck gate (entry for arrival surges; exit for end-of-day congestion). Use gate utilization to decide which.
Stagger demand (e.g., off-peak promotions) to flatten arrival clusters.
Match usable capacity to demand to cut denials.
Future work: multiple replications with confidence intervals; CSV export; in-UI gate/arrival editing.

## Slide 14
Thank You
Questions?
slow_entry bottleneck
entry wait 127→52 min
+1 entry gate
exit_congestion bottleneck
exit wait 119→18 min
+1 exit gate → 2× throughput
rush_hour 2×2 map
throughput 10→17.3 veh/hr
(+72%)
limited_slots
13 denied vehicles
100% occupancy
86 automated tests passing · python3 -m unittest